CHEMICAL SPILL PROCEDURES TEMPLATE

The range and quantity of hazardous substances used in Georgia Tech teaching and research laboratories  make it impossible to provide a single all-encompassing plan for dealing with chemical/biological incidents.  Each operating unit is expected to deal with minor spills (see definitions, below) occurring in their area.   This requires pre-planning and training/rehearsal.

This document provides a template for the development of an individualized spill response plan. Download it and modify the document to suit your needs.

1.  Types of Spills:

a.  Minor Spills are those which can be handled by the operating unit.

b. Major Spills are those which require notification of or assistance from other agencies.  A spill automatically becomes "major" in the following instances:

- There is a fire, or the threat of fire, outside of a controlled space (fume hood).

-  There is a personnel injury or exposure likely to require medical assistance.

-  The spill involves unknown or highly reactive material.

-  There is a release of a toxic or flammable gas outside of a controlled space.

2.  Personnel to Be Notified:

| Position | Name | Work Phone | Home/Cell Phone |
| --- | --- | --- | --- |
| Lab Manager |  |  |  |
| Primary Investigator |  |  |  |
| Building Manager |  |  |  |
| Georgia Tech Police |  | (404) 894-2500 or 911 |  |
| GT EH&S |  | (404) 216-5237 |  |
| Add Lines As Needed |  |  |  |

3.  Spill Control/Containment Material/Supplies for this laboratory are __[provide location]_____________. (See Appendix A for a recommended list of materials/supplies).

4.  Minor Chemical Spill Procedures:

  - Alert people in the immediate area of spill.

  - Avoid breathing vapors from spill.

  - Put on protective equipment, including safety goggles, suitable gloves, and long sleeved lab coat.

  - Confine spill to small area.

  - Use appropriate materials to neutralize and absorb inorganic acids and bases.

  - For other liquids, absorb spill with vermiculite, dry sand, or adsorbent pads.

  - For solid spills.  Cover the spill with a slightly damp paper towel to avoid creating a cloud of dust, Push the material into a dustpan or other instrument using the towel- do not use a broom/dust brush.

  - Collect material, used adsorbents/neutralizing agents, etc. in a polyethylene bucket or bag.

  - Call EH&S (4-6224) to arrange for collection and disposal of spill residue.

5.  Major Chemical Spill Procedures:

- Attend to injured or contaminated persons and remove them from exposure.

- Alert people in the area to evacuate.  If danger is believed sufficient - pull the fire alarm and evacuate the building.

- If spill material is flammable, turn off ignition and heat sources if that can be done safely.

- Close doors to affected area.

- Call Georgia Tech Police (404) 894-2500. Provide as much of the following as is known.

  - What chemical(s) are involved.

  - How much was spilled.

  - Where the spill is located.

  - Nature of any injuries.

  - What control measures have been taken.

  - Your name and phone number (or where you will be located).

- Meet responders.

6.  Type of Material/Clean-Up Procedure: The table below provides a synopsis of type chemicals that may be spilled and recommended clean-up materials.  This list should be amended to add any chemicals requiring special procedures.  As always, the MSDS on the particular chemical is a preferable reference.  If you choose to purchase, pre-packaged, commercially available spill kits, the clean-up procedures should be modified to reflect specifics, e.g., Acid Spills: Use container "A" from spill supplies in accordance with directions on the package.

QUICK REFERENCE FOR SPILL CLEANUPS

| Chemical Spilled | Clean-Up Procedures |
| --- | --- |
| Acids, organic | Apply sodium bicarbonate. Adsorb with spill pillow or vermiculite. |
| Acids, inorganic | Apply sodium bicarbonate/Calcium Oxide or sodium carbonate/calcium oxide. Adsorb with spill pillow or vermiculite. NOTE: Hydrofluoric acid is an exception to the general practice, see below. |
| Acid Chlorides | Do not use water. Absorb with sand or sodium bicarbonate. |
| Aldehydes | Absorb with spill pillow or vermiculite. |
| Aliphatic Amines | Apply sodium bisulfite. Adsorb with spill pillow or vermiculite. |
| Aromatic Amines | Absorb with spill pillow or vermiculite. Avoid skin contact or inhalation. |
| Aromatic Halogenated Amines | Absorb with spill pillow or vermiculite. Avoid skin contact or inhalation. |
| Azides | Absorb with spill pillow or vermiculite. Neutralize with 10% ceric ammonium nitrate solution. |
| Bases (caustic alkalis) | Neutralize with acid, citric acid, or commercial chemical neutralizers. Absorb with spill pillow or vermiculite. |
| Carbon Disulfide | Adsorb with spill pillow or vermiculite. |
| Chlorohydrins | Absorb with spill pillow or vermiculite. Avoid skin contact or inhalation. |
| Cyanides | Cover solids with damp paper towel and push onto dust pan or use a HEPA filter vacuum to collect the solids. Absorb liquids with spill pillow or vermiculite. |
| Halides, organic or inorganic | Apply sodium bicarbonate. |
| Halogenated Hydrocarbons | Absorb with spill pillows or vermiculite. |
| Hydrazine | Avoid organic matter. Apply "slaked lime". Adsorb with spill pillow or vermiculite. |
| Hydrofluoric Acid | Adsorb with calcium carbonate (limestone) or lime (calcium oxide) rather than sodium bicarbonate. The use of sodium bicarbonate will lead to the formation of sodium fluoride, which is considerably more toxic than calcium fluoride. Be careful in the use of spill pillows used to adsorb the acid. Some pillows contain silicates which are incompatible with hydrofluoric acid. |
| Inorganic Salt Solutions | Apply soda ash |
| Mercaptans/Organic Sulfides | Neutralize with calcium hypochlorite solution. Absorb with spill pillow or vermiculite. |
| Nitriles | Sweep up solids. Absorb liquids with spill pillows or vermiculite. |
| Nanoparticles | Pick up particles with a HEPA or ULPA filtered vacuum. |
| Nitro compounds/Organic Nitriles | Absorb with spill pillow or vermiculite. Avoid skin contact or inhalation. |
| Oxidizing Agents | Apply sodium bisulfite. |
| Peroxides | Absorb with spill pillow or vermiculite. |
| Phosphates, organic and related | Absorb with spill pillow or vermiculite. |
| Reducing Substances | Apply soda ash or sodium bicarbonate. |

APPENDIX A

Spill Clean Up Materials

Each laboratory/or operating unit should have at least enough material to handle spill of 1 LT/1 KG (or the largest container in inventory) or all chemicals on-hand. In addition, each laboratory, especially those with floor drains should have spill socks, pillows, pads or bulk absorbant to contain spilled material.

Kits may be built from raw materials, see table in basic document for type materials.

Purchased as individual items or as composite kits from suppliers such as VWR or Lab Safety.

The table below (courtesy of Bio-Engineering) are the contents of a spill kit for a typical laboratory.

| Material | Spill Type | What it Does |
| --- | --- | --- |
| Mercury Adsorb Powder | Elemental Mercury | Converts elemental mercury on work surfaces, in cracks, and hard to reach places into metal/mercury amalgam. |
| Dry Acid Neutralizer | All acids except HF | Neutralizes Acids |
| Dry Hydrofluoric Acid Neutralizer | Hydrofluoric Acid | Neutralizes Hydrofluoric Acid |
| Dry Base Neutralizer | Bases/Caustics | Neutralizes Bases |
| Formaldehyde Polymerizer | Formaldehyde/Formalin | Reacts with water based formaldehyde solutions to form a nontoxic, polynoxyline polymer which yields a plastic like solid |
| Activated Carbon | Flammable Solvents | Cleans up flammable solvent spills and suppresses hazardous vapors |
| Solid-A-Sorb | All Spills Except HF | Mixes well with water and oil based substances |
| Sorbant Pads | Liquids | Quickly contains small spills |
| Sorbant Socks or Booms | Liquids | Quickly contains larger spills. |